## Slide 1: MVCP Exercise solving class

## Slide 2: Capacity calculations

## Slide 3: Answer the following questions
If the planned capacity use is 100 pcs/day, and we would like to keep a 20% capacity cushion, what should be a designed capacity?
Given our actual output 105 pcs per day, compute the utilisation (designed capacity as calculated above).
Calculate the efficiency in the same working system if there is a daily 30 minutes of allowance, and production time is 3 minutes per piece.

## Slide 4: Solution
0,2=DC/100-1 DC=120
105/120=87.5%
105/(120-30/3)=95.45%

## Slide 5: Calculation of the expected resource (=expected resource)
We have 3 machines
There are 3 shifts per day (8 hrs per shift)
There are 45 minutes time allowances per shift and per machine
There are 250 working days in a year
Performance percentage is 90%.
Calculate the Designed Capacity, the Effective Capacity and the Expected Resource quantity.
Calculate the capacity cushion, if we are planning to use only 800,000 minutes during the whole year.

## Slide 6: Solution
DC = 250*3*8*60*3=1,080,000
EC = DC – 3*3*45*250 = 978,750
R = 0,9*EC = 880,875
C.cushion = DC / 800,000 – 1 = 35%

## Slide 7: Linear programing

## Slide 8: Find the TR and profit maximizing product mixes
 | P1 | P2 | b (hs/y)
R1 | 2 | 4 | 7000
R2 | 5 | 2 | 6500
R3 | 2 | 2 | 5000
MIN (pcs/y) | 400 | 500 | 
MAX (pcs/y) | 1000 | 1500 | 
P ($/pcs) | 120 | 40 | 
CM($/pcs) | 30 | 30 | 

## Slide 9: Find the TR and profit maximizing product mixes
 | P1 | P2 | b (hs/y)
R1 | 2 | 4 | 4000
R2 | 2 | 2 | 3000
R3 | 0 | 2 | 5000
MIN (pcs/y) | 100 | 0 | 
MAX (pcs/y) | 1000 | 800 | 
P ($/pcs) | 100 | 50 | 
CM($/pcs) | 60 | 30 | 

## Slide 10: Other product mix decisions
One resource – one product
Bottleneck
Competing products

## Slide 11: Find the TR and profit maximizing product mixes
 | P1 | P2 | P3 | P4 | P5 | b (hrs/y)
R1 | 6 |  |  |  |  | 3 000
R2 |  | 3 | 2 | 1 |  | 3 000
R3 |  |  |  |  | 5 | 1 000
R4 |  |  |  |  | 6 | 6 000
R5 |  |  |  |  | 4 | 5 000
MIN (pcs/y) | 0 | 200 | 100 | 250 | 400 | 
MAX (pcs/y) | 400 | 500 | 400 | 1000 | 2000 | 
p (HUF/pcs) | 200 | 100 | 400 | 100 | 50 | 
cm (HUF/pcs) | -50 | 80 | 40 | 30 | 20 | 

## Slide 12: Scheduling

## Slide 13: 1st part
Product | Processing time (day) | Due date (day)
A | 10 | 12
B | 7 | 10
C | 8 | 6
D | 12 | 20
E | 11 | 15
A workstation has to produce 5 different products. Processing times and due dates for each product is contained by the matrix below.
a) Determine the proper sequence of the products with the help of using
FCFS rule: ……-……-……..-……-……..
SPT rule: ……-……-……..-……-…….
EDD rule: ……-……-……..-……-…….
CR rule: ……-……-……..-……-…….

## Slide 14: 2nd part
 | Aft | At | Aj
FCFS | ……………… | ……………… | ………………
SPT | ……………… | ……………… | ………………
EDD | ……………… | ……………… | ………………
CR | ……………… | ……………… | ………………
b) Determine the average flow time, average tardiness, and average number of jobs at the work center.
c) Compare the results of the four rules? Which is the best? Why?