Product and Process Management

Scheduling

Exercise 1

A workstation has to produce 4 different products’ processing time and due date for each product is contained by the matrix below.

| Product | Processing time (day) | Due date (day) |
| --- | --- | --- |
| A | 14 | 20 |
| B | 10 | 16 |
| C | 7 | 15 |
| D | 6 | 17 |

a) Determine the proper sequence of the products with the help of using

FCFS rule: ……-……-……..-……

SPT rule: ……-……-……..-……

EDD rule: ……-……-……..-……

CR rule: ……-……-……..-……

b) Determine the average flow time, average tardiness, and average number of jobs at the work center.

|  | Aft | At | Aj |
| --- | --- | --- | --- |
| FCFS | ……………… | ……………… | ……………… |
| SPT | ……………… | ……………… | ……………… |
| EDD | ……………… | ……………… | ……………… |
| CR | ……………… | ……………… | ……………… |

c) Compare the results of the four rules? Which is the best? Why?

……………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

Exercise 2

The matrix below contains information about a workstation’s job.

|  | Processing time (hours) | Pieces/task | Setup time (hours) | Due date (hours) |
| --- | --- | --- | --- | --- |
| A……………. | 0,14 | 45 | 0,7 | 4 |
| B……………. | 0,25 | 14 | 0,5 | 10 |
| C……………. | 0,1 | 18 | 0,2 | 12 |
| D…………… | 0,25 | 40 | 10 | 20 |
| E…………….. | 0,1 | 75 | 0,5 | 15 |

Determine the total job time for each job by computing the total processing time for the job and then adding in the setup time.

a) Identify the processing  sequence that would result using

FCFS rule: ……-……-……..-…….-……

SPT rule: ……-……-……..-…….-……

EDD rule: ……-……-……..-…….-……

CR rule:……-……-……..-…….-……

b) ) For each method determine the average flow time, average tardiness, and average number of jobs at work center!

|  | Aft | At | Aj |
| --- | --- | --- | --- |
| FCFS | ……………… | ……………… | ……………… |
| SPT | ……………… | ……………… | ……………… |
| EDD | ……………… | ……………… | ……………… |
| CR | ……………… | ……………… | ……………… |

c) Compare the results of the four rules? Which is the best? Why?

……………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

Exercise 3

A wholesale household equipment distribution center uses a two-step process to fill orders. Information about seven orders is contained by the table below.

| Order | Time (hours) |
| --- | --- |
|  | Step 1 | Step 2 |
| A | 1,2 | 1,4 |
| B | 0,9 | 1,3 |
| C | 2,0 | 0,8 |
| D | 1,7 | 1,5 |
| E | 1,6 | 1,8 |
| F | 2,2 | 1,75 |
| G | 1,3 | 1,4 |

a) Determine the job sequence that will minimize the time required to fill the orders.	……-…….-……-……-…...-……-……

b) Determine the total flow time of filling orders.  	………hours

Exercise 4

The table below contains information about the schedule of a pooler center.

| Product | Cleaning | POLÍROZÁS |
| --- | --- | --- |
|  | Start | Finish | Start | Finish |
| A | 0 | 2 | 2 | 5 |
| B | 2 | 6 | 6 | 9 |
| C | 6 | 11 | 11 | 13 |
| D | 11 | 15 | 15 | 20 |
| E | 15 | 17 | 20 | 23 |
| F | 17 | 20 | 23 | 24 |
| G | 20 | 21 | 24 | 28 |

a) Determine a schedule that will result in earlier completion of all jobs on this list

……-…….-……-……-…...-……-……

b) Determine the total flow time. 	…………..min

Solution

Exercise 1

a)

FCFS(A,B,C,D

SPT(D,C,B,A

EDD(C,B,D,A

| Product | Processing time (day) | Due date (day) | CR1 | CR2 | CR3 | CR4 |
| --- | --- | --- | --- | --- | --- | --- |
| A | 14 | 20 | 1,429 | first | first | first |
| B | 10 | 16 | 1,600 | 0,200 | -0,5 | -1,1 |
| C | 7 | 15 | 2,143 | 0,143 | second | second |
| D | 6 | 17 | 2,833 | 0,500 | -0,66667 | third |

CR(A,C,D,B

b)

|  | Aft | At | Aj |
| --- | --- | --- | --- |
| FCFS | 26,50 | 11,00 | 2,86 |
| SPT | 19,75 | 6,00 | 2,14 |
| EDD | 21,00 | 6,00 | 2,27 |
| CR | 24,75 | 9,25 | 2,68 |

Exercise 2

a)

FCFS(A,B,C,D,E

SPT(C,B,A,E,D

EDD(A,D,C,B

| Product | Processing time (day) | Due date (day) | CR1 | CR2 | CR3 | CR4 | CR5 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | 7 | 4 | 0,571 | first | first | first | first | first |
| B | 4 | 10 | 2,500 | 0,75 | -4,25 | -4,75 | fourth | fourth |
| C | 2 | 12 | 6,000 | 2,5 | -7,5 | third | third | third |
| D | 20 | 20 | 1,000 | 0,65 | second | second | second | second |
| E | 8 | 15 | 1,875 | 1 | -1,5 | -1,75 | -2,075 | fifth |

CR(A,D,C,B,E

Exercise 3

a) B, A, G, E, F, C, D

0,9       2,1      3,4            5                 7,2              9,2           10,9

| B | A | G | E | F | C | D |
| --- | --- | --- | --- | --- | --- | --- |

|  | B | A | G | E |  | F | C | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

0,9      2,2         3,6        5             6,8 7,2         8,98    9,75      11,25

b) total flow time 11,25 óra

Exercise 4

| Product | Time (hours) |
| --- | --- |
|  | Step 1 | Step 2 |
| A | 2 | 3 |
| B | 4 | 3 |
| C | 5 | 2 |
| D | 4 | 5 |
| E | 2 | 3 |
| F | 3 | 1 |
| G | 1 | 4 |

a) G,E,A, D,C,B,F b) 22 hours